## Slide 1: Data assimilation for microscale pollutant atmospheric dispersion
Eliott Lumet, Mélanie Rochoux, Thomas Jaravel, Simon Lacroix and Olivier Vermorel
HARMO21
27 september 2022

## Slide 2: Introduction
Context: Build high-fidelity models for microscale dispersion in urban environment and improve them thanks to mathematical methods
    Study case: One neutral trial of the MUST field campaign (Yee and Biltoft. 2004)
    Large-Eddy Simulation (LES) model:
      Realistic representation of the urban canopy
      Resolution of turbulence large scales
      Temporal evolution of the plume
Instantaneous concentration field timelapse obtained with LES of the MUST experiment #2681829
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 3: Introduction
Need for a stochastic approach to represent the envelope of possible events
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion
Impact of the wind direction angle on the mean velocity field and on the 0.01-ppm contour line of average concentration
Boundary
Conditions
Modelling
error
Pollutant source
These models may remain inaccurate in spite of
their high cost
Context: Build high-fidelity models for microscale dispersion in urban environment and improve them thanks to mathematical methods
    CFD dispersion model uncertainties:

## Slide 4: Introduction
In situ measurements
LES model
DA
Develop a data assimilation framework to quantify and reduce the LES uncertainties
Optimal plume
estimation
    Classical method in meteorology/climate
    Emerging idea for atmospheric CFD models
    ex: Lucas et al. 2015, Mons et al. 2017, Sousa et al. 2018, Defforge et al. 2019, Aristodemou et al. 2019
Objective:

## Slide 5: Introduction
  Objective: Estimate best the mean concentration field given uncertain and
Sensors
LES model
DA
Improved estimation of the parameters
Optimal plume estimation
In situ measurements
Prior uncertain parameters
In situ measurements
LES model estimation
LES model
  Issue #1: Parameter estimation
    For steady state estimation, LES models depend more on parameters than initial conditions
Problem formulation
    The estimation targets are the model parameters
    Resolution of an inverse problem

## Slide 6: Introduction
  Objective: Estimate best the mean concentration field given uncertain and
In situ measurements
LES model estimation
  Issue #1: Parameter estimation
  Issue #2: Cost of the LES model
    The LES model is too expensive Replace it by a surrogate in the data assimilation workflow
Problem formulation
Sensors
LES model
DA
Optimal plume estimation
In situ measurements
Prior uncertain parameters
LES model
Sensors
DA
Optimal plume estimation
In situ measurements
Prior uncertain parameters
Surrogate model
LES model
Surrogate model
Offline training

## Slide 7
{60s spin-up + 200s}
20 000 hCPU
Model setup:
  Solver: AVBP for LES of compressible flows and low-Mach flows
  Subgrid-scale model: WALE (wall adapted)
Model computational cost:
The LES model is too expensive for data assimilation
Inflow
Outflow
Symmetry
Wall laws
Symmetry
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion
I. LES model
  Unstructured mesh of 90 millions tetrahedra:
    Refinement near obstacles:
    30 cm at least 15 cells per obstacle edge

## Slide 8: I. LES model
Inflow boundary condition
  Prescribed mean velocity profile:
    With: (data from Yee and Biltoft. 2004)
    (fitted on experimental data)
  Constant wind direction:
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 9: I. LES model
  Turbulence injection:
    Method: Synthetic eddy method (Smirnov et al. 2001)
Inflow boundary condition
  Prescribed mean velocity profile:
    With: (data from Yee and Biltoft. 2004)
    (fitted on experimental data)
  Constant wind direction:

## Slide 10: I. LES model
i. The site topography is
assumed to be well known
Selection of uncertain parameters
  Objective: Choose which parameters should be corrected by Data Assimilation
Boundary
Conditions
- Inlet mean wind direction:
- Friction velocity imposed in the inlet log-profile:
- Ground roughness:
- Reynolds stress tensor imposed with the turbulence injection:
Modelling
error
Pollutant source
- Source location:
- Pollutant emissions:
- Numerical scheme
- SGS model
Not considered in this first study
These inner parameters have less impact than BCs parameters
ii. Turbulence injection parameter
do not have significant impacts
on predictions
Reconstruction of only two parameters:
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 11: II. Surrogate model
  Halton sequence: splitted into train and test samples
Training process
  Ensemble of LES to sample the parameter space: budget of 100 LES 2 500 000 hCPU
Need to calibrate the RBF surrogate using the training samples
New parameters
Fast prediction of
Surrogate model
We limit this first study to a horizontal cut of the concentration field
RBF Interpolator (Scipy)
Interpolates as a linear combination of radial basis functions
One regression problem per grid point (scales badly)

## Slide 12: II. Surrogate model
Validation process:
  Comparison of concentration field predictions: worst case
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion
This test sample is very close to the parameter space edge
RMSE = 9.07 ppm The error is large on the plume edge

## Slide 13: II. Surrogate model
Validation process:
  Comparison of concentration field predictions: best case
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion
RMSE = 0.19 ppm Building interactions are well reproduced
1 surrogate integration 0.125s with 1 CPU

## Slide 14
Sensors
Synthetic experiment:
Synthetic observations
DA
Surrogate model
Surrogate model
Prior parameters knowledge
Truth parameters
?
?
Truth system state
= unknown
Truth system state
= known
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion
III. Data assimilation results
  Are we able to retrieve the correct parameters?
  Is the analysis equal to the truth ?

## Slide 15
Parameter estimation results:
  DA algorithm: Iterative Ensemble Kalman Filter
    Number of members:
    Number of sensors:
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion
  The data assimilation algorithm works well and is able
  to correct the inflow boundary conditions.
III. Data assimilation results
Assimilation

## Slide 16
Concentration results field:
  Mean concentration isolines comparison:
The plume shape is
well estimated
Algorithm execution
time = 100s
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion
III. Data assimilation results

## Slide 17: Conclusion
Take-home messages
  1) Data assimilation provides a powerful framework to reduce inflow boundary condition uncertainties in microscale LES simulations.
  2) Replacing the LES model by a surrogate model opens the way towards a real-time data assimilation framework to better predict plume behaviour in case of accident.
Perspectives
  Extend the approach to 3D fields by using state-of-the-art surrogate model (dimension reduction combined with gaussian process regression)
  Extend the approach to estimate source uncertainties
  Use model sensitivity analysis for optimal sensor placement
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 18: Appendices

## Slide 19: Appendice I: Why do we use LES instead of RANS?
Technical & historical reasons specific to my lab
  At CERFACS, AVBP a LES solver is developed and maintained
  In my team, a LES intercomparison of the MUST case has already been performed (Rochoux et al. 2021)
LES superiority for UQ perspectives
  LES model requires less parametrization
  LES model errors are less important (LES intercomparison study)
  Easier Uncertainty Quantification framework
LES would allow to further development in the future
  We kept unsteady moving averages to try outs sensor positioning methods for plume developing scenario
  LES allow to predict more fields than RANS:
    Concentration high order statistics, peak concentration: useful data for analysis
    Frozen AVBP: need for stress tensors for specific surrogate modeling
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 20: Appendice II: TurboMUST
Model adaptation
  Domain rotation using TurboAVBP:
    Goal: Keep symmetry BCs // to the flow streamwise direction
    Principle:
      - Split the domain in two
      - Coupled resolution on both domain
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 21: Appendice II: TurboMUST
Model results
  Metrics computed for all sensors where:
Metric | FB (ppm) | RMSE (ppm) | FAC2 | MG | VG
Perfect model | 0 | 0 | 100% | 1 | 1
LES Model | -0.048 | 0.002 | 91% | 1.24 | 1.57
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 22: Appendice III: Turbulence injection method
Principle
Precursor
Simulation
CL périodiques
Champ libre (sans obstacles)
Maillage quads
Convergence statistique
Rescaling
Turbulence Injection
  Good agreement with experimental fluctuations data
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 23: Appendice III: Turbulence injection method
Velocity fluctuations profiles | 
Tower S | Tower T
Results
  Overall good agreement with experimental data
  Lack of TKE over the canopy
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 24: Appendice III: Turbulence injection method
Turbulence spectrum | 
Tower S | Tower T
Results
  Fine reproduction of the turbulence
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 25: Appendice IV: Uncertain parameter space definition
Perturbed Physics Ensemble
  Goal: Sample the parameter space to build a surrogate model
  Method: Halton sequence (low-discrepancy)
  What ranges of variation for uncertain parameters?
    Microclimatology based on 12 days of acquisition by one MUST SAMS station:
    Constraints on the wind direction:
      - Limited simulations budget
      - The plume must pass through the containers
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 26: Appendice V: Surrogate model results
Metrics averaged over all the validation samples:
  For each sample the metrics are computed by comparison between the surrogate and the LES estimations
  The scores below are the averages of all these metrics computations
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion
Metric | MAE (ppm) | RMSE (ppm) | MG | VG | FMS(1ppm)
Score | 0.189 | 1.585 | 0.949 | 1.105 | 0.878

## Slide 27: Appendice VI: IEnKF algorithm for parameter estimation
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 28: Appendice VII: Concentration anamorphosis
Issue: is always positive The EnKF hypothesis are not verified
Solution: - Assume that and thus follow a log-normal distribution
      - Assimilate “log-concentration” obs: so that
Changes in the EnKF algorithm:
  Sample log-concentration observations with correct moments:
  , with and
  and
  Note that the observation error covariance matrix R is also changed by the anamophosis
  Update the general observation operator:
Liu et al.
2017
Detection threshold: Avoid giving too much weight to low concentrations obs
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 29: Appendice VIII: Other Data Assimilation results
Metrics results:
  Quantify the misft between the truth concentration field and the ones from data assimilation
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion
Metric | FB (ppm) | RMSE (ppm) | VG
Background | -3.12e-01 | 1.75E+01 | 4.34
Analysis | -3.55E-04 | 1.22E-02 | 1.00

## Slide 30: Appendice VIII: Other Data Assimilation results
Concentration fields results:
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 31: Appendice VIII: Other Data Assimilation results
Concentration estimations at probes locations:
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 32: Appendice VIII: Other Data Assimilation results
Evolution of the parameters estimation:
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion

## Slide 33: Appendice IX: Sensitivity Analysis
Sobol Indices:
Eliott Lumet et al. 2022 – Data assimilation for microscale pollutant atmospheric dispersion